## Slide 1: COSMOS 2019 State Machines

## Slide 2: Roadmap
Lab 3 review
New C tricks:
  Switch/case
  rand()
State Machines
  States vs events
  State machines as models
State Machine Activities
Lab 4

## Slide 3: Event-Driven Programming

## Slide 4: Event-Driven Programming
So far, you’ve used code that:
  runs once, at startup
  Runs forever in a while loop
But some code should run only at specific times:
  Periodic sensor monitoring
  React to warnings
  Take advantage of opportunities
  Respond to requests

## Slide 5: Asynchronous vs Synchronous
Synchronous:
  Code runs at periodic intervals
Asynchronous:
  Run when an event occurs
    Receives an event from another process
    Event is “consumed”

## Slide 6: Reactive Architecture
Events:
  Generated by event checkers
    Pieces of code (or hardware)
  r, generated by services
  Are fed to services
Services:
  Pieces of code that react to events
    Services “consume” the events

## Slide 7: Ingredients of an Event Checker
Must remember previous measurement
  Cannot detect change from 1 measurement
  Needs persistent memory (static)
  We call this memory the checker’s “state”
Must compare previous state to current measurement
  That’s what a change is, right?
If current measurement != previous measurement:
  Make previous = current
  Generate an event

## Slide 8: Event checker:

## Slide 9: Ingredients of a Service
When an event occurs:
  Call service, pass in event
  Service does some action
  “consume” (ie, destroy) the event

## Slide 10: Simple Reactive Architecture in C
Events are signaled with high-scope variables
  Boolean flags?
  Integers to signal one of several events?
Event Checkers set the high-scope variables
Main loop polls high-scope variables
  Calls appropriate service
  then clears variable

## Slide 11: Simple Reactive Architecture in C

## Slide 12: States and Events

## Slide 13: States vs Events
State:
  Temporary but not instantaneous property of a system
    For example: Sleeping, Awake, Dead
Events:
  Instantaneous
    Can be internally caused changes in state:
      For example: WAKE_UP, FALL_ASLEEP, DIE
    Or momentary occurrences that don’t necessarily cause changes in state:
      For example, WAKEUP_ALARM_RECEIVED
    Or external causes of changes:
      For example: BULLET_RECEIVED

## Slide 14: State Machine:
A set of states, linked by a set of transitions (generally events):

## Slide 15: State Machine Diagrams
A way of drawing state machines
Standardized in Unified Modeling Language notation (UML)
  States are bubbles
    Starting state denoted by dot
  Transitions are arrows
  EVENTS are written on arrows
    Can have / associated actions
  Conditional transitions are diamonds
    Take path of true [guard condition]

## Slide 16: State Machines as Models
Model of the physical world:
  Used to abstract (simplify) a complex system
    Example: Button is up, button is down
Software Design Model
  Used to plan, document, and build code
    Or circuits, or machines
    Example: Button event checker from last lecture
  Easy to observe and debug (SO USEFUL)

## Slide 17: Physical Models
https://www.uml-diagrams.org/examples

## Slide 18: Behavioral Models
The principles of collective animal behaviour
D.J.T Sumpter Phil. Trans. R. Soc. B 29 January 2006

## Slide 19: Server Design Models
http://www.cs.dartmouth.edu/~campbell/cs60/srt.html

## Slide 20: Physical Design Models

## Slide 21: Electrical Design Models

## Slide 22
Synchronous SMs:
All event checkers are synchronous SMs
  Event checkers need memory!
Run periodically
  In a timer ISR
  In your main loop
  Transitions are NOT events
  Instead, they are conditions
    (observations of some other system’s state)

## Slide 23: Question: Are either of these legit?

## Slide 24: State Machines in C:

## Slide 25: State Machines Activities:
Activity 1:
  As a class, Model alarm Clock as SM
Activity 2:
  In groups of ~5, Design a state machine for an oven on imaginary hardware:
    4 buttons, 8 events
      You may name the buttons whatever you like
    1 screen to display whatever you, the designers, would like
    User must be able to set temperature, cook time, cook mode
    User must be able to stop cooking at any time

## Slide 26: Lab 4 hints
One state at a time!
  Test as you go!
To get a random number between 0 and 1000, do:
  “ rand() % 1001 “
Don’t forget “break;”
For the SM design portion:
  Stop coding while you design the SM!

## Slide 27: Lab 4 teams
['Natalie ', 'Max ']
['Florence', 'Helen ']
['Wonjin ', 'Afra ']
['Austin ', 'Abhigna ']
['Jose ', 'Ashvin ']
['JJ ', 'Natasha ']
['Lillian ', 'Andrew ']
['Julia ', 'Serena ']
['Namya ', 'Kelly ']
['Shize ', 'Annie ']
['Steven ', 'Joshua ']
['Aaron ', 'Tianyi ', 'Katie ']

## Slide 28: State Machine Activity
Activity 1:
  As a class, Model alarm Clock as SM
Activity 2:
  In groups of ~5, Design a state machine for an oven on imaginary hardware:
    4 buttons, 8 events
      You may name the buttons whatever you like
    1 screen to display whatever you, the designers, would like
    User must be able to set temperature, cook time, cook mode
    User must be able to stop cooking at any time

## Slide 29: COSMOS Timeline
This week:
  Monday: State machine workshop, start lab 4
  Tuesday: Robot Quest
  Wednesday, Thursday: Lab 4
  Friday: Pick Group Projects
Week 3:
  Monday – Thursday: Group Project Work
  Friday: Finalize posters (?)
Week 4:
  Integrate group projects